## Slide 1: Real time pitch shifting
Lkham Nyambuu – Alexis Mermet – Cyril Cadoux

## Slide 2: Introduction
Transform speech audio files into higher- or lower-pitched voices
Satisfy the real time constraints
  Only partial information is available (1 chunk of small size)
  Computations must be very fast
Solutions :
  Use look up tables
  Use integers variables as often as possible

## Slide 3: First method : Robot Voice
Motivation : It is the simplest method possible
How it works :
  A LUT (the same length than a chunk) stores SINE values at a given frequency
  Multiply each chunk by the corresponding value in the LUT (modulation)
Small detail : We must remove the direct component
  Use the simplest high-pass filter :

## Slide 4: Second Method : Granular Synthesis
Motivation :
  The ‘aliasing effect’ is what makes the robot voice so special
  But if the shifting frequency is too high, the intelligibility becomes too poor
  Find a method that uses no ‘explicit’ modulation
How it works :
  Use interpolation to create new samples at a higher rate (ie resampling)
  Playing those samples at the input-rate will stretch the audio and make it deeper
  A few raw samples are used twice, in two different grains
  Use a tapered window to merge the overlapping resampled values of consecutive grains

## Slide 5: Example

## Slide 6: Examples

## Slide 7: Third Method : Add LPC coefficients to GS
Motivation :
  Granular Synthesis works well, but the resulting speech sounds un-natural
  Find a way to preserve the energy envelope during the transformation
Good model : with the excitation and the resonator
How it works:
  Obtain coefficients from input and deduce
  Apply granular synthesis on those samples
  Compute with and